NMI "i-Series"

Ultrasonic level meter, consisting of ultrasonic

sensor with temperature sensor to compensate

ultrasound transit time and built-in free

programmable evaluation electronic.

Encapsulated, permanently immersible sensor in
corrosion-proof enclosure with high chemical

resistance.

Suitable for measurement of liquids and

pasty media.

Measurement range:	0.125 to 3 m

Measurement

uncertainty:	0.25% of measurement range

(distance sensor - surface)

Resolution:	1 mm

Startup time:	4 sec. until output of readings

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357; (option: PVDF)

Temperature range:	-40 °C to max. +80 °C

Fastening:	rear thread 1"

optional: front thread 1.5"

Protection:	IP 68

Immersion

detection:	with SUB sleeve (optional)

Ex protection:	Ex mb for Zone 1

Ex ia for Zone 0 (optional)

Output:	4 - 20 mA / HART

Cable length:	10 m; (option: 20/30 m)

can be extended up to 1000 m

Model:	NMI0 03

Deliver, install ready to use and calibrate

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Ultrasonic level meter, consisting of ultrasonic

sensor with temperature sensor to compensate

ultrasound transit time and built-in free

programmable evaluation electronic.

Encapsulated, permanently immersible sensor in
corrosion-proof enclosure with high chemical

resistance.

Suitable for measurement of liquids and

pasty media.

Measurement range:	0.3 to 6 m

Measurement

uncertainty:	0.25% of measurement range

(distance sensor - surface)

Resolution:	2 mm

Startup time:	4 sec. until output of readings

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357; (option: PVDF)

Temperature range:	-40 °C to max. +80 °C

Fastening:	rear thread 1"

optional: front thread 1.5"

Protection:	IP 68

Immersion

detection:	with SUB sleeve (optional)

Ex protection:	Ex mb for Zone 1

Ex ia for Zone 0 (optional)

Output:	4 - 20 mA / HART

Cable length:	10 m; (option: 20/30 m)

can be extended up to 1000 m

Model:	NMI0 06

Deliver, install ready to use and calibrate

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Ultrasonic level meter, consisting of ultrasonic

sensor with temperature sensor to compensate

ultrasound transit time and built-in free

programmable evaluation electronic.

Encapsulated, permanently immersible sensor in
corrosion-proof enclosure with high chemical

resistance.

Suitable for measurement of liquids and

pasty media.

Measurement range:	0.3 – 10 m

Measurement

uncertainty:	0.25% of measurement range

(distance sensor - surface)

Resolution:	3 mm

Startup time:	4 sec. until output of readings

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357; (option: PVDF)

Temperature range:	-40 °C to max. +80 °C

Fastening:	rear thread 1"

optional: front thread 2"

Protection:	IP 68

Immersion

detection:	with SUB sleeve (optional)

Ex protection:	Ex mb for Zone 1

Ex ia for Zone 0 (optional)

Output:	4 - 20 mA / HART

Cable length:	10 m (option: 20/30 m),

can be extended up to 1000 m

Model:	NMI0 10

Deliver, install ready to use and calibrate

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Ultrasonic level meter, consisting of ultrasonic

sensor with temperature sensor to compensate

ultrasound transit time and built-in free

programmable evaluation electronic.

Encapsulated, permanently immersible sensor in
corrosion-proof enclosure with high chemical

resistance.

Suitable for measurement of liquids and

pasty media.

Measurement range:	0.5 – 15 m

Measurement

uncertainty:	0.25% of measurement range

(distance sensor - surface)

Resolution:	5 mm

Startup time:	4 sec. until output of readings

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357; (option: PVDF)

Temperature range:	-40 °C to max. +80 °C

Fastening:	rear thread 1"

Protection:	IP 68

Immersion

detection:	with SUB sleeve (optional)

Ex protection:	Ex mb for Zone 1

Ex ia for Zone 0 (optional)

Output:	4 - 20 mA / HART

Cable length:	10 m; (option: 20/30 m)

can be extended up to 1000 m

Model:	NMI0 15

Deliver, install ready to use and calibrate

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Overvoltage protection for sensor lines

High-performance overvoltage limiter with

coarse and fine protection for symmetric or

galvanically isolated data line inputs and outputs

as well as 2-wire technology.

Suitable for transmission frequencies up to 600kHz

and 0.5A operating current.

Internal self-control using failsafe diodes

which short-out data lines in case of error.

Maintenance-free due to high electronic

overdimensioning

Nominal leakage

surge current:	20 kA (8/20 µs)

Maximum

operating voltage:	28 V DC / 20 V AC

Protection rating:	36 V wire-ground

Installation:	35 mm DIN rail

Enclosure:	plastic

Model:	DataPro 2x1-24/24V

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Programming modem

Box with built-in HART modem for reprogramming,

optimisation and readout of parameters from

NMi sensors.

No additional power adapter or separate HART

resistor required.

Direct power supply of the connected sensor to program

via the USB interface of the PC/laptop.

Box with integrated HART resistor, USB-A-

plug and 80 cm cable for connection to PC/laptop

plus 30 cm cable with service clamps for direct,

tool-free connection with sensor cable.

Incl. CD with software HART PC for setting and saving

of parameters, echo image analysis, recording of image 
and echo history

Model:	ZUB0 HART BOX 04

Deliver and install ready to use

Type:............................

Make:.....................

Qty:  1 Pc.	UP: ..................

TP: ....................

Modem adapter

Adapter for direct connection of NMi sensors

with plug, types NL or PCM, to HART-Box 04

Models:	ZUB0 HART ADAP 01 (for NivuLog)

ZUB0 HART ADAP 02 (for PCM)

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................