The tender texts below comprise the most common solutions in practice so that options and parts that are not required can be deleted and only quantities need to be inserted.

For certain projects it is recommended to edit the texts. Our experienced colleagues will be pleased to support you competently, quick and free of charge when it comes to create your tender texts. Please contact us via sales@nivus.com or by phone: +49 7262 9191-794.

NivuFlow 750

Flow rate measurement of slight to heavily 
polluted media in part filled and full pipes 
as well as varying canal profiles.

Detection of the water surface level as well as individual,

spatially allocated flow velocities.

Flow transmitter with integrated numeric

discharge models for determination of the average

flow velocity from up to 144 individual flow velocities

(Type M9 required!).

Connection options and calculation functions for

up to 9 flow velocity sensors to determine the

the exact flow profile distribution in large or

structured canals (Type M9 required!).

Optionally free programming of up to 3 different

measurement places with different shapes,

dimensions, sensor types, sensor quantities and Ex-protection

with just one transmitter (Type M9 required!).

Detection of spatially allocated flow velocity profiles

using the correlation method and digital

pattern detection.

Calculation of the real 3D flow profile by

integrating all measured local velocities covering

the wetted cross section.

Calculation of the flow rate from average flow velocity,

filling level and canal shape considering

medium temperature, flume shape, flume dimensions

and degree of partial filling based on internal

numeric discharge models.

Storage, graphic representation and transmission

of all relevant readings.

Determination of the water surface level using ultrasound

from the bottom up using the sensor’s built-in pressure cell,

ultrasound from top down or by using separate level meters.

Several level measurement methods can be combined to

achieve the best possible adjustment of the measurement to

high measuring dynamics and hydraulically difficult applications

as well as for redundant detection under critical conditions.

Step controller optimised for discharge control with automatic

flush function and sensor sedimentation monitoring.

Slide valve monitoring regarding torque and runtime.

Energy-saving cycle operation mode for DC measurement systems

without external power supply with free selectable 
measurement/sleep cycles.
Switchover between cycle mode to event mode

for high-resolution detection of critical flow rates digitally

controlled and based on limit values.
Event mode free programmable for short cycle or permanent
measurements.

Temperature compensation of all readings.
Metal-encapsulated compact enclosure with easily accessible

plug-in spring cage terminals on the front panel for

quick tool-free installation and mounting.

Large daylight TFT full colour graphic display featuring

240 x 320 px and 65536 colours.

Optimum display clarity even in direct sunlight thanks to

1:400 contrast ratio and up to 80° possible deviation

from observation plane in any direction.

Graphic 3D representation of the velocity distribution.

Modern and intuitive one-hand operation using rotary

pushbutton in context with high-resolution graphic

colour display.

Programming with flat hierarchical structure, supported

by colours and graphic elements, visual true-to-scale

representation even of complex canal shapes and sensor 
positions in order to avoid errors during commissioning.

Intelligent error and sensor diagnostics.

Integrated recorder function with min. and max. memory.

Storage of all individual velocities and according position

heights, levels, average flow velocities, flow rates, medium

and air temperature in internal high capacity memory.

Programming data and all saved readings as well as errors

can be copied to standard USB stick via front-side

USB interface.

HART interface for direct connection of compatible

sensors.

Connection of the transmitter to following systems using

HART, RS232/485, TCP-IP/Ethernet and ModBus TCP/RTU.

Worldwide connectivity via mobile radio through

integrated MultiRoam SIM chip as well as additional

SIM card slot (option).

Direct transmission of measurement and system data,

error messages and alarms via mobile radio to the NIVUS

web portal.

Remote maintenance, remote diagnostics and remote

commissioning with the full scope of services of the on-site

commissioning.

Online access using Internet browser without the need to

install additional software.

Integration of the transmitter into higher systems

via ModBus TCP/RTU

Operating voltage: 	85 – 240 V AC

9 – 36 V DC (optional)

9 – 36 V DC cycle operation 
	(option)

Construction:	DIN rail

Enclosure material:	profile aluminium

Protection:	IP 20

Ex Protection:	using Ex separator Type iXT

Display:	full colour graphic TFT daylight display

240 x 320 px, 65536 colours

contrast min. 1:400

Programming:	dialog mode using rotary pushbutton

and 2 function keys

Versions: 	NF7-5S1 (for 1x v-sensor)

NF7-5SR (for 1x v-sensor +
control)

NF7-5M3 (for up to 3 v-sensors)

NF7-SM9 (for up to 9 v-sensors

or up to 3 different measurement places with

different sensor types, sensor quantities and

variable programming)

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Licence Key

For device-related transmission of measurement data 
via FTP and/or e-mail to customer server or free
selectable e-mail address.

Transfer of the serial number-based access data for

the activation of a NivuFlow measurement

transmitter by the operator.

Version:	NFX0 LIZENZ FTP

Transmit access data via e-mail

Type: ............................

Make: .....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Robust, corrosion-proof field enclosure with large

transparent cover for NF 550 and one optional

Ex-Separation Module.

Special enclosure with enhanced protection degree

for outdoor installation of the transmitter.

Material:	plastic

Protection:	IP 67 or
	IP 68 (optional)

Versions:	ZUB0 NFW0

ZUB0 NFW0 IP68

Deliver incl. accompanying cable glands, install

transmitter and isolating amplifier if required and

install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Ex module for direct connection of Type POA/CS2

flow velocity sensors, Type EBM Electronic Box,

Type LUS level sensor as well as NivuBar Plus

Ex-protected HART-interface for direct connection

of i-Series level sensors

Module for safe separation of Ex areas between

Ex-compatible sensors and Type NF 750 transmitters.

Ex module can be installed in a distance of up to 300 m

from the transmitter in separate protective enclosure

Operating voltage: 	12 V DC (from NivuFlow 750)

Construction:	DIN rail

Enclosure material:	plastic

Protection:	IP 20 (DIN rail)
Ex Protection:	Zone 1

Max. distance

Sensor – iXT:	150 m

Max. distance

iXT – NF750:	300 m

Versions: 	iXT0 210 (1x v, AUS and mA each)

iXT0 211 (1x v, AUS and HART)

iXT0 420 (3x v, 1xAUS, 1x mA)

iXT0 421 (3x v, 1xAUS 1x HART)

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Multiplexer module for connection of multiple

sensors on site to reduce wiring efforts and to extend

the distance between sensors and transmitter.

Connection of up to 3 Type POA/CS2

flow velocity sensors, Type EBM Electronic Box,

Type LUS level sensor as well as NivuBar Plus

level sensor.

An ultrasonic i-Series level sensor can be connected

additionally via HART.

Module can be installed in a distance of up to 1000 m

from the transmitter in separate protective enclosure

(extra power adapter an coupling relay on site required).

Operating voltage: 	12 V DC (from NivuFlow 750)

Construction:	DIN rail

Enclosure material:	plastic

Protection:	IP 20

Max. distance

sensor – MPX:	150 m

Max. distance

MPX – NF750:	1000 m

Version: 	MPX0 421

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

DIN rail power adapter to operate MPX multiplexer,

auxiliary relay and flow velocity / level sensors on site

in the remote installation.

Operating voltage:	230 V AC

Secondary voltage:	24V DC; 25 VA

Protection:	IP 43

Version:	OCP ZNT GPRS

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

DIN rail relay to control MPX multiplexer and flow

velocity / level sensors on site in the remote installation.

To operate the DIN rail relay a sufficient power adapter

such as Type OCP ZNT GPRS is required

Operating voltage:	12 V DC

SPDT:	1x; 6A/250 V

Mounting width:	6.2 mm

Protection:	IP 20

Version:	ZUB0 REL 12V

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for installation on

channel bottom, channel side or floating installation

from top down.

Detection of up to 16 spatially allocated flow velocities

using built-in ultrasonic sensor.

Measurement range:	- 100 cm/s to 600 cm/s

Meas. uncertainty:	1 % of measurement range

Materials:	stainless steel 1.4571; PPO GF30

PEEK, PE, PU

Protection:	IP 68

Ex Approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 150 m

Version:	POA-V200KT

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Flow-optimised combi sensor for installation on

channel bottom or floating installation from top down.

Detection of flow level and up to 16 spatially allocated

flow velocities using two built-in independent ultrasonic

sensors.

Measurement ranges

Flow velocity:	- 100 cm/s to 600 cm/s

Water ultrasound:	4 – 200 cm

Meas. uncertainties

Flow velocity:	1 % of measurement range

Water ultrasound:	better than 2 mm

Materials:	stainless steel 1.4571; PPO GF30

PEEK, PE, PU

Protection:	IP 68

Ex Approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 150 m

Version:	POA-V2H1KT

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor with built-in

pressure measurement cell for installation on

channel bottom or channel side.

Detection of up to 16 spatially allocated flow velocities

using built-in ultrasonic sensor.

Additional detection of flow levels using built-in

pressure measurement cell with high chemical resistance

Measurement ranges

Flow velocity:	- 100 cm/s to 600 cm/s

Pressure cell:	0 – 350 cm  level

Meas. uncertainties

Flow velocity:	1 % of measurement range

Pressure cell:	max. 0.75 % zero point drift of MR

max. 0.5 % of final value

Materials:	stainless steel 1.4571; PPO GF30

PEEK, PE, PU

Protection:	IP 68

Ex Approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30 m)

extendable up to 150 m using

pressure compensation element

Version:	POA-V2D0K

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Flow-optimised combi sensor with built-in

pressure measurement cell for installation on

channel bottom.

Detection of flow level and up to 16 spatially allocated

flow velocities using two built-in independent ultrasonic

sensors.

Additional detection of flow levels using built-in

pressure measurement cell with high chemical resistance

Measurement ranges

Flow velocity:	- 100 cm/s to 600 cm/s

Water ultrasound	4 – 200 cm

Pressure cell:	0 – 350 cm

Meas. uncertainties

Flow velocity:	1 % of measurement range

Water ultrasound:	better than 2 mm

Pressure cell:	max. 0.75 % zero point drift of MR

max. 0.5 % of final value

Materials:	stainless steel 1.4571; PPO GF30

PEEK, PE, PU

Protection:	IP 68

Ex Approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30 m)

extendable up to 150 m using

pressure compensation element

Version:	POA-V2U1K

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for

installation on the channel bottom, channel side or for

floating installation

Detection of up to 16 individual, spatially allocated flow

velocities using built-in ultrasonic sensors

Measurement range:	- 100 cm/s to 600 cm/s

Meas. uncertainty:	1 % of measurement range

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 250 m

Model:	CS2-V200 KT

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for

installation on the channel bottom or for

floating installation

Detection of up to 16 individual, spatially allocated flow

velocities using built-in ultrasonic sensor

Flow level detection using two redundant ultrasonic

sensors

Measurement ranges

flow velocity:	- 100 cm/s to 600 cm/s

Water-ultrasound:	12 – 400 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Water-ultrasound:	better than 2 mm

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 250 m

Model:	CS2-V2H1 KT

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for

installation on the channel bottom or channel side

Detection of up to 16 individual, spatially allocated flow

velocities using built-in ultrasonic sensor

Flow level detection using sensor-integrated

pressure measurement cell with high chemical resistance

Measurement ranges

Flow velocity:	- 100 cm/s to 600 cm/s

Pressure cell:	0 – 350 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Pressure cell:	max. 0.75 % zero point drift/MR

max. 0.5 % of final value

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30 m)

via pressure compensation element 
extendable to up to 250 m

Model:	CS2-V2D0 KT

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor with additional 
pressure measurement cell for installation on the channel

bottom

Detection of up to 16 individual, spatially allocated flow

velocities using built-in ultrasonic  sensor

Flow level detection using two redundant ultrasonic

sensors as well as an additional sensor-integrated

pressure measurement cell with high chemical resistance

Measurement ranges

Flow velocity:	- 100 cm/s to 600 cm/s

Water ultrasound:	12 – 400 cm

Pressure cell:	0 – 350 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Water-ultrasound:	better than 2 mm

Pressure cell:	max. 0.75 % zero point drift/MR

max. 0.5 % of final value

Materials:	stainless steel 1.4571; PPO GF30

PA6 GF30, CFK, PU

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (Option: 15/20/30 m)

via pressure compensation element 
extendable to up to 250 m

Model:	CS2-V2U1 KT

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised velocity sensor for installation through

the pipe wall in part filled and full pipes

Detection of up to 16 individual, spatially allocated flow

velocities using built-in ultrasonic sensor

Installation using welding nozzle with 1 ½“ screw-in thread, 
retaining element and stop ball valve (option)

Meas. ranges:	- 100 cm/s to 600 cm/s

Meas. uncertainty:	1 % of measurement range

Materials:	stainless steel 1.4571; PPO GF30

PEEK, PE, PU

Pipe length:	200 mm (option: 300 mm if ball valve
is used)

Protection:	IP 68

Ex-approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 150 m

Version:	POA-V200R

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Flow-optimised combi sensor for installation through the 
pipe wall into the bottom of part filled and full pipes

Detection of flow level as well as up to 16 individual,

spatially allocated flow velocities using two built-in

independent ultrasonic sensors.

Installation using welding nozzle with 1 ½“ screw-in thread, 
retaining element and stop ball valve (option)

Meas. ranges:	- 100 cm/s to 600 cm/s

4 – 200 cm height

Meas. uncertainty:	1 % of measurement range (v)

better than 2 mm (water-ultrasound)

Materials:	stainless steel 1.4571; PPO GF30

PEEK, PE, PU

Pipe length:	200 mm (option: 300 mm if ball valve
is used)

Protection:	IP 68

Ex-Approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 150 m

Version:	POA-V2H1R

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for

installation through the pipe wall into the bottom of

part filled and full pipes

Detection of up to 16 individual, spatially allocated flow

velocities using built-in ultrasonic sensor

Installation using welding nozzle with 1 ½“ screw-in thread, 
retaining element and stop ball valve (option)

Measurement range:	- 100 cm/s to 600 cm/s

Meas. uncertainty:	1 % of measurement range

Materials:	stainless steel 1.4571, PEEK, PE, PU

Pipe length:	200 mm (option: 300 if ball valve is used)

Protection:	IP 68

Ex approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

extendable up to 250 m

Model:	CS2-V100 RP

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Air-ultrasonic sensor for level measurement from top down,

suitable for direct connection to NivuFlow 750 or

Ex separator module iXT

Measurement range:	10 – 200 cm

Dead zone:	10 cm

Meas. uncertainty:	lower than 5 mm

Materials:	Stainless steel 1.4571; PPO GF30

PEEK, PE, PU

Protection:	IP 68

Ex-Approval:	Zone 1 (option)

Cable length:	10 m (option: 15/20/30/50/100 m)

Version:	OCL-L1KS12

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Ultrasonic level meter, consisting of ultrasonic

sensor with temperature sensor to compensate

ultrasound transit time and built-in free

programmable evaluation electronic.

Encapsulated, permanently immersible sensor in
corrosion-proof enclosure with high chemical

resistance.

Suitable for measurement of liquids and

pasty media.

Measurement range:	0.3 to 6 m

Measurement:	4 mm over the entire

uncertainty	measurement range

Resolution:	2 mm

Start time:	4 sec. to readings output

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357; (option: PVDF)

Temperature range:	-40 to max. +80 °C

Fastening:	rear thread 1“

option: front thread 1.5“

Protection:	IP 68

Immersion	with SUB sleeve (optional)

detection:

Ex protection:	Ex mb for Zone 1

(option)	Ex ia for Zone 0

Output:	4 - 20 mA / HART

Cable length:	10 m; (option: 20/30/50/100 m)

can be extended up to 1000 m

Model:	NMI0 06

Deliver, install ready to use according to manufacturer specifications

and program according to application requirements

Type: ............................

Make: .....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Sensor line overvoltage protection

Lightning and overvoltage protection for potential-free

data lines, according to DWA A-M 261 suitable as

overvoltage protection for wastewater treatment plants

High-performance overvoltage limiter with

coarse and fine protection, with minimum internal

resistance, particularly adjusted to LUS and POA sensors

Internal self-control using failsafe diodes

Maintenance-free due to high electronic

Nominal leakage

surge current

(8/20 µs):	20 kA

Max. operation

voltage:	12 V DC/24 V DC

Series resistance:	0.3 Ohm

Installation:	35 mm DIN rail

Enclosure:	plastic

Ex approval:	Zone 1 (option)

Models:	1x DataPro 2x1-12V/12V

1x SonicPro 3x1-24/24V

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Analog output overvoltage protection

Lightning and overvoltage protection for potential-free

data lines

High-performance overvoltage limiter with

coarse and fine protection for symmetric or

galvanically isolated data line inputs and

outputs as well as for 2-wire systems

Suitable for transmission frequencies up to 600 kHz

and 0.5 A operating current

Internal self-control using failsafe diodes

which short-out data lines in case of error.

Maintenance-free due to high electronic

overdimensioning

Nominal leakage

surge current

(8/20 µs):	20 kA

Maximum

operating voltage:	28 V DC / 20 V AC

Protection rating:	36 V wire-ground

Installation:	35mm DIN rail

Enclosure:	plastic

Ex approval:	Zone 1 (option)

Model:	DataPro 2x1-24/24V

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Power lines overvoltage protection

High-performance overvoltage limiter

for 230 V AC power inputs with 16 A current,

according to DWA A-M 261 suitable as

overvoltage protection for wastewater treatment plants

Overvoltage protection with very high leakage capacity.

Varistor self-control and independent disconnection

from mains in case of  exceeding leakage currents.

Visual indication of operation and malfunction

Nominal leakage

current wire-ground:	20 KA

Maximum

operating voltage:	300 V AC

Protection rating:	1.1 kV wire-ground

Installation:	35 mm DIN rail

Enclosure:	Polycarbonate

Model:	EnerPro 220 Tr/20

Deliver and install ready to use

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Accessories

Tapping saddle with nozzle 1.5” and gasket

for later installation of flow velocity sensors in pipelines with

various wall materials such as cast, plastic,

concrete, steel/stainless steel etc.

Outer pipe

diameter:	........... mm

Material:	1.4301 and NBR (gasket)

Version:	ZUB0ABS

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Welding nozzle, straight construction with

RP1 1½” inner thread

Suitable for installation of pipe sensors 1.5”

in pipelines

Material:	1.4571

(option: steel)

Version:	ZUB0 STU15

Deliver and install

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Full port ball valve for removal of pipe sensors from

full filled pipes without pressure

Mounted using an 1½"screw-in thread

Material:	1.4571

Version:	ZUB0 HAHN R15

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Pressure compensation element

For connection or to extend sensors

Types V2U and V2D.

Consisting of junction box made of metal incl. clamps,

Pressure compensation plug and socket as well as large

air filter with visual self-control for absorption

of air humidity.

Enclosure:	Al die-cast

Protection:	IP 65 (enclosure)

IP 40 (filter)

Type:	ZUB0 DAE

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ....................

Pipe measuring section with welding neck flanges, dome

and maintenance opening.

1½" weld-in socket for admission of flow velocity sensor,

installation on pipe bottom or off-centred depending on

expected sedimentation

Nominal diameter:	DN ...

Material:	zinc-plated steel
(option: stainless steel 1.4571)

Dome height:	depending on impoundage pressure,

however 500 mm min.

Flange angle: 	....° from center

Accessories:	plastic flange DN 200 with

boring 1"

flange gasket

Deliver and install ready to use incl. all required small parts

Type:............................

Make:.....................

Qty.:  1 pc.	UP: ..................

TP: ...................

Wedge support left 30° for POA and CS2 sensors.

Suitable for sideways mounting and exactly perpendicular

vertical alignment of the flow velocity wedge sensors

for correct velocity path distribution according to

Gauss.

Material:	stainless steel 1.4571

Version:	ZUB0 KS00 L30 V4A

Deliver incl. required corrosion-proof mounting material

and install ready to use according to manufacturer 
specifications

Type: ............................

Make: .....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Wedge support right 30° for POA and CS2 sensors.

Suitable for sideways mounting and exactly perpendicular

vertical alignment of the flow velocity wedge sensors

for correct velocity path distribution according to

Gauss.

Material:	stainless steel 1.4571

Version:	ZUB0 KS00 R30 V4A

Deliver incl. required corrosion-proof mounting material

and install ready to use according to manufacturer 
specifications

Type: ............................

Make: .....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Initial start-up of measurement place carried out by

manufacturer.

Verification of hydraulic suitability of the place of installation,

correct sensor mounting and installation of transmitter

Handover of parameter lists containing implemented

instrument setup and initial start-up protocol.

Prerequisite for commissioning:

Sensors installed according to manufacturer specifications

and transmitters wired ready for operation.

Qty.:  1 flatrate	UP: xxxxxxxxxx

TP: ....................