The tender texts below comprise the most common solutions in practice so that options and parts that are not required can be deleted and only quantities need to be inserted.

For certain projects it is recommended to edit the texts. Our experienced colleagues will be pleased to support you competently, quick and free of charge when it comes to create your tender texts. Please contact us via sales@nivus.com or by phone: +49 7262 9191-794.

NivuFlow Mobile 750

Portable flow rate measurement with extremely long

battery life independent from mains power, integrated

data logger and GPRS modem for remote data transmission,

limit value alerting and device diagnostics, suitable for

use and programming in Ex zone 1.

Flow rate measurement in full and part filled pipes and

any canal profile.

Detection of the water surface level as well as

spatially allocated flow profiles using correlation methods

and digital pattern detection.

Measurement of flow level, flow velocity and

medium temperature.

If used with CSM sensors:

Detection of low volumes in small and medium

pipes and any canal profile.

Measurement particularly conceived for the detection of

low volumes of wastewater, dirty water and surface

water in the field of extraneous water and seepage water

measurement; for influent control, measurement places

for billing purposes and similar applications.

Flow-dynamic calculation of very low volumes

once the sensor has fallen dry based on the gravity line

principle by automatic consideration of the slope

prevailing at the measurement place as well as the variable

viscosity of the medium to measure and the flume

roughness.

Calculation of the real 3D flow profile by

integrating up to 48 local velocities covering

the wetted cross section.

Temperature compensation of all measurement values.

Calculation of the flow rate from average flow velocity,

filling level and canal shape considering

medium temperature, flume shape, flume dimensions

and degree of partial filling based on internal

numeric discharge models.

Connection options and calculation functions for

up to 3 flow velocity sensors to determine the accurate

distribution of flow profiles in large ore segmented

canals.

Determination of the water surface level using ultrasound

from the bottom up using the sensor’s built-in pressure cell,

ultrasound from top down or by using separate level meters.

Several level measurement methods can be combined to

achieve the best possible adjustment of the measurement to

high measuring dynamics and hydraulically difficult applications

as well as for redundant detection under

critical measurement conditions.

Programming, representation of readings and data

transmission via secured, password-protected 
WLAN connection without the need to open the unit.

Programming optional via separate display and operation 
module Type ZAB 01 or via standard Smartphone,

Tablet or Laptop with Android, Windows or iOS.

Internal storage and transmission of all relevant

measurement data.

Delay-free and event-based detection of measurement

values including switchover of measurement cycles via

digital input.

Options for continuous output of flow rate,

flow velocity or medium temperature

on free scalable analogue output.

Output of free programmable flow rate impulses,

event-related messages or limit values via digital output.

Rugged, shock-proof, absolutely water-tight compact

plastic enclosure suitable for use in wastewater.

Redundant power supply thanks to 2 easily replaceable

gas-tight rechargeable batteries with double plug-in

connection.

Options for additional external power supply

via power adapter, solar panel, fuel cell,

extra batteries or similar .

Integrated LED visible from the outside for easy visual

identification of instrument status and error messages

without the need to open the transmitter

Modern, intuitive operation using external touchscreen.

Automatic sensor detection and indication of article no.,

serial no. and sensor type.

Reconciliation of the measurement system to improve

accuracy by automatically reading the calibrated

sensor-specific parameters.

All connected types of level sensor types are detected

automatically.

Quick start assistant with automatic subdivision of

level measurement areas depending on the

programmed profile and canal dimensions.

Programming with flat hierarchical structure, supported

by colours and graphic elements, visual true-to-scale

representation even of complex canal shapes and sensor 
positions in order to avoid errors during commissioning.

Intelligent error and sensor diagnostics.

Integrated recorder function with min. and max. memory.

Storage of all individual velocities, levels, average

flow velocities, flow rates and medium temperature in

internal high capacity memory.

Additional options to store up to 3external analogue

signals such as level, overflow volumes, reference values

etc. as well as a digital input (counter, runtime).

Programming and all saved readings and errors can be

read out via WLAN or using an USB stick.

Protection:	IP 68 (closed)

IP 67 (lid open)

Power supply:	1/2 replaceable rechargeable lead,

gel batteries, 12 V DC/14 Ah each

Battery life:	up to 18 months without replacement

Internal data 	up to 182 000 data sets

memory:

Max. memory	20 years with 60 min. cycle

capacity:

Meas. modes:	Interval, constant, event

Interval, event, constant

Storage interval:	separately adjustable intervals for

normal and event operation.
Interval cycles:	5, 10, 15, 20 and 30 seconds
	1, 3, 5, 10, 15, 20, 30 and 60
	minutes

Data transmission:	via WLAN, USB stick or
internal LTE modem (optional).
remote data transmission to 
available NIVUS WEB Portal

Inputs:	1x V or combi sensor

1x ultrasonic level via DSM

2 x 0/4-20 mA (active)

1x 0/4-20 mA (passive)

1x digital input (active)

1x power adapter/alternative 
power supply

Outputs: 	1x voltage output 0-10 V

1x digital output (SPDT)

1x USB-A interface for
USB stick

Connection:	via water-tight, corrosion proof

IP 68 plug connectors.
	Integrated automatic sensor detection

with article no., serial no., sensor type

and sensor-adjusted parameters.

Material:	glass-fibre reinforced plastic

Weight:	approx. 2.2 kg (without battery)

Version:	NFM-0750 000 (no Ex, no internal

LTE modem)

NFM-0750 G0E (no Ex, with internal

LTE modem)

NFM-0750 0EE (Ex, no internal

LTE modem)

NFM-0750 GEE (Ex, with internal

LTE modem)

Transmitter incl. memory stick, activation magnet and

screwdriver to open the battery compartment

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Data transmission fee for the NIVUS devices Type

NFM with integrated LTE modem and NLG.

Required tariff after the free 12-month data transmission 
included with the purchase of a new NFM or NLG

has expired.

Transmission of readings to the NIVUS WebPortal

or via NIVUS data kiosk to a customer system.

Shortest permissibe

measurement cycle:	1 minute

Shortest permissibe

transmission cycle:	1 hour

Period of notice:	3 months to the end of the

contract period

Total contract

period:	……… years

Version:	SNI0CONNECT01

Unlock fort he device in use

Type: ............................

Make: .....................

Qty.:  1 	UP: ..................

TP: ....................

Licence Key

For device-related transmission of measurement 
data using a customer SIM card via FTP and/or 
e-mail to customer server or free selectable 
e-mail address.

Provision of access data for NFM unlocking by

operator.

Version:	NFM0 LIZENZ FTP

Provision of access data by e-mail

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Gas-tight rechargeable battery with built-in double

plug-in connection for quick battery replacement.

Designed for long-term optimised power supply
of the portable NFM 750 transmitter.

Type:	lead gel

Voltage:	12 V DC

Capacity:	14 Ah

Weight:	approx. 4.0 kg

Version:	NFM0 ZAPB 1215

Deliver

Type:............................

Make:.....................

Qty.:  2 Pcs.	UP: ..................

TP: ....................

Power adapter with charging tray for rechargeable

battery Type NFM0 ZAPB 1215 and as extra

power supply for NFM.

Version:	NFM0 ZLAD

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Display and operating module for NFM series

IP67-certified 8" outdoor tablet

Resolution:	1280 x 800

Operation:	touchscreen

Operating system:	Android

Communication:	WLAN, USB, Bluetooth,
2G, 3G and 4G.

Version:	NFM0 ZAB0 1

Deliver and install ready to use

Type:............................

Make:.....................

Qty:  1 Pc.	UP: ..................

TP: ....................

Sensors

Mini flow velocity sensor for detection of

very low flow rates in small pipe and canal dimensions.

Minimised sensor body with a height of 20 mm and a

length of 72 mm made of robust and long-life plastic

without built-in electronic components for centred or

lateral installation on pipe or canal bottom.

Sensor installation in pipes possible starting at 150 mm

diameter.

Sensor suitable for detection of flow velocity profiles

starting even at flow levels as low as 30 mm using

built-in ultrasonic sensor.

Detection of up to 16 individual, spatially allocated

flow velocities.

Measurement range:	-100 cm/s to 600 cm/s

Meas. uncertainty:	1 % of measurement range

Materials:	stainless steel 1.4571 (AISI 316Ti), 
PVDF, PA, PU

Protection:	IP 68

Ex protection:	Zone 1

Cable length:	7 m, with integrated plug for

connection to NFM or

NFM0 ZAB 2VKK adapter box

Version:	CSM-V100 KT

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Mini combi sensor for installation on the canal bottom.

Minimised sensor body with a height of 24 mm and a

length of 210 mm made of robust and long-life plastic

for centred or lateral installation on pipe or canal bottom.

Sensor suitable for detection of flow velocity profiles

starting even at flow levels as low as 55 mm using built-in

ultrasonic sensor.

Detection of flow level using built-in pressure cell.

Detection of average flow velocity by measuring up to

16 individual, spatially allocated flow velocities using

ultrasonic cross correlation and digital pattern recognition.

Sensor installation in pipes possible starting at 150 mm

diameter.

Measurement range:	-100 cm/s to 600 cm/s

0 – 500 cm (level)

Meas. uncertainty:	1 % of measurement range (v)

better than 0.5% of measurement

range (h)

Material:	Polyurethane, stainless steel 1.4571

(AISI 316Ti), PPO GF30, PA

Protection:	IP 68

Ex protection:	Zone 1 (optional)

Cable length:	7 m (optional: 15m), with integrated 
plug for connection to NFM or

NFM0 ZAB 2VKK adapter box

Cable connection:	assembled plug with flood-proof

pressure compensation element and

easily replaceable silica gel 
drying capsules

Version:	CSM-V1D0 KT

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Ultrasonic mini sensor for contactless detection of

very low flow levels in small pipe and canal dimensions.

Minimum block distance 40 mm measured from

mounting plate (pipe crown)

Minimised sensor body with a height of as low as 24 mm

Sensor with 2 level sensors switching over automatically

in vertically and horizontally beaming mounting position

with sound deflection mirror to achieve minimum block

distances in almost full canals.

Made of robust and long-life plastic without built-in

electronic components for installation on pipe crown.

Sensor installation in pipes possible starting at 160 mm

diameter.

Measurement range:	0 – 200 cm

Block distance:	4 cm

Meas. uncertainty:	lower than 5 mm

Materials:	stainless steel 1.4571 (AISI 316Ti); 
PU

Protection:	IP 68

Ex protection:	Zone 1 (optional)

Cable length:	7 m (optional: 15m), with integrated 
plug for connection to NFM

Version:	DSM-L0KS 12

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor for installation

on flume bottom or flume side.

Detection of up to 16 individual, spatially allocated

flow velocities using built-in ultrasonic sensor.

Recommended for use in pipes and flumes starting at

DN 1000.

Measurement range:	-100 cm/s to 600 cm/s

Meas. uncertainty:	1 % of measurement range

Materials:	stainless steel 1.4571 (AISI 316Ti); 
PPO GF30, PA6 GF30, CFK, PU

Protection:	IP 68

Ex protection:	Zone 1 (optional)

Cable length:	7 m (optional: 15m), with integrated 
plug for connection to NFM or

NFM0 ZAB 2VKK adapter box

Version:	CSP V200 KT

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised combi sensor for installation

on flume bottom.

Detection of up to 16 individual, spatially allocated

flow velocities using built-in ultrasonic sensor.

Detection of flow level using two redundant ultrasonic

sensors.

Recommended for use in pipes and flumes starting at

DN 1000.

Flow velocity

measurement range:	-100 cm/s to 600 cm/s

Water-ultrasound:	12 – 400 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Water-ultrasound:	better than 2 mm

Materials:	stainless steel 1.4571 (AISI 316Ti); 
PPO GF30, PA6 GF30, CFK, PU

Protection:	IP 68

Ex protection:	Zone 1 (optional)

Cable length:	7 m (optional: 15m), with integrated 
plug for connection to NFM or

NFM0 ZAB 2VKK adapter box

Version:	CSP V2H1 KT

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised flow velocity sensor with pressure cell

for installation on flume bottom or flume side.

Detection of up to 16 individual, spatially allocated

flow velocities using built-in ultrasonic sensor.

Detection of flow level using built-in pressure cell

featuring high chemical resistance.

Recommended for use in pipes and flumes starting at

DN 1000.

Flow velocity

measurement range:	-100 cm/s to 600 cm/s

Pressure cell:	0 – 500 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Pressure cell:	max. 0.75 % zero point drift/MR

max. 0.5 % of final value

Materials:	stainless steel 1.4571 (AISI 316Ti); 
PPO GF30, PA6 GF30, CFK, PU

Protection:	IP 68

Ex protection:	Zone 1 (optional)

Cable length:	7 m (optional: 15m), with integrated 
plug for connection to NFM or

NFM0 ZAB 2VKK adapter box

Cable connection:	assembled plug with flood-proof

pressure compensation element and

easily replaceable silica gel 
drying capsules

Version:	CSP V2D0 KT

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Flow-optimised combi sensor with extra pressure cell

for installation on flume bottom.

Detection of up to 16 individual, spatially allocated

flow velocities using built-in ultrasonic sensor.

Detection of flow level using two redundant ultrasonic

sensors and a built-in extra pressure cell featuring high

chemical resistance.

Recommended for use in pipes and flumes starting at

DN 1000.

Flow velocity

measurement range:	-100 cm/s to 600 cm/s

Water-ultrasound:	12 – 400 cm

Pressure cell:	0 – 500 cm

Meas. uncertainties

flow velocity:	1 % of measurement range

Water-ultrasound:	better than 2 mm

Pressure cell:	max. 0.75 % zero point drift/MR

max. 0.5 % of final value

Materials:	stainless steel 1.4571 (AISI 316Ti); 
PPO GF30, PA6 GF30, CFK, PU

Protection:	IP 68

Ex protection:	Zone 1 (optional)

Cable length:	7 m (optional: 15m), with integrated 
plug for connection to NFM or

NFM0 ZAB 2VKK adapter box

Cable connection:	assembled plug with flood-proof

pressure compensation element and

easily replaceable silica gel 
drying capsules

Version:	CSP V2U1 KT

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Ultrasonic level sensor with integrated

temperature sensor to compensate

ultrasound transit time and built-in free

programmable evaluation electronics.

Encapsulated, permanently immersible sensor in
corrosion-proof enclosure with high chemical

resistance.

Measurement range:	0.3 to 6 m

Meas. uncertainty:	4 mm over the entire

measurement range

Resolution:	2 mm

Start time:	4 sec. to readings output

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357

Temperature range:	-50 to max. +80 °C

Fastening:	rear thread 1“

Protection:	IP 68

Ex protection: 	Ex ib for Zone 1 (optional)

Output:	4 - 20 mA / HART

Cable length:	5 m; (optional: 10/20/30 m), with 
integrated plug for connection to NFM

Version:	NMI0 06

Deliver, install ready to use according to manufacturer

specifications and set up according to application

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Hydrostatic suspension probe for level measurement

Measurement cell:	ceramic

Measurement range:	0-4 m wc (optional: 0-6 m wc,

0-10 m wc)

Ex protection:	ATEX Zone 1 (optional)

Cable length:	10 m (Option: 20/30 m)

Cable connection:	assembled plug with flood-proof

pressure compensation element and

easily replaceable silica gel 
drying capsules

Version:	HSB0 NBP0

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Corrosion-proof straining clamp for

suspension of cables from 7.5 to 10.5 mm.

Material:	1.4571

Model:	AKL 1

Deliver and install ready to use according to manufacturer 
specifications together with hydrostatic probe

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Adapter box for velocity measurement using

3 v-sensors with NFM.

Robust, break-proof plastic box with 2 sensor 
connection sockets and connection cable incl. plug
for connection to NFM.

Materials:	stainless steel 1.4571 (AISI 316Ti);

GFK, PU

Protection:	IP 67

Sensor connection:	2 sensor sockets, covered by

water-tight protective caps

Ex protection:	Zone 1

Cable length:	0.3 m with fixed and encapsulated
plug for direct connection to NFM

Version:	NFM0 ZAB 2VKK

Deliver incl. mounting plate for fastening on hoop guards

and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Intrinsically safe T-shape antenna for remote data

transmission with fixed cable and water-tight 
IP 68 plug for direct connection to NFM 750.

Protection:	IP 68

Ex-Protection:	Ex ib for zone 1

Cable length:	2.5 m with integrated plug for
connection to NFM

Version:	NFM0 ZANT 1

Deliver, install and connect ready to use according 
to manufacturer specifications

Type: ............................

Make: .....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Instructions on handling, installation, setting of

parameters and data evaluation of NFM 750 under

real measurement place conditions

(if available and provided).

Duration:	6 hours

Qty.:  Flat Rate	UP: xxxxxxxxxxx

TP: ....................

Accessories

NFM suspension device for fastening

on step irons

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZHAK NFM0 2

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

NFM suspension device for fastening

on step irons incl. 2 integrated suspension brackets

for coiled sensor cables.

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZHAK NFM0 1

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Hoop guards for mechanical protection of NFM connection

plugs in harsh environments such as shafts, canals,

industrial plants etc.

Suitable for additional fastening of a Connector Box Type

NFM0 ZVS1 or an Adapter Box Type NFM0 ZAB 2VKK.

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZSBL IRE

Deliver incl. fastening material and install on NFM

ready to use

Type:............................

Make:.....................

Qty.:  1 Pair	UP: ..................

TP: ....................

Connector Box for parallel connection of multiple

input and output signals as well as an alternative

power supply to NFM.

Robust, break-proof plastic box with connection

cable incl. plug for connection to NFM.

Material:	stainless steel 1.4571 (AISI 316Ti);

GFK, PU

Protection:	IP 67

Connections:	1 socket for alternative power

supply

4 cable glands for external signals

Cable length:	0.2 m with fixed and encapsulated plug

for direct connection to NFM

Version:	NFM0 ZVS1

Deliver incl. mounting plate for fastening on hoop guards

and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pre-configured cable with plug and open

cable ends for direct connection of inputs and

outputs to NFM without Connector Box

Plug protection:	IP68

Cable length:	10 m

Cable connection:	one side with pre-configured plug
	one side with open cable ends

Versions:	NFM0 ZVER AEA for active
analog input

NFM0 ZVER AEP for passive
analog input

NFM0 ZVER AA for analog 
output

NFM0 ZVER DE for digital 
input

NFM0 ZVER DA for digital 
output

NFM0 ZVER MU for all inputs
and outputs

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pre-configured cable with plug and open

cable ends for alternative external NFM

power supply via solar panel, fuel cell,

external batteries, rechargeable batteries etc.

Plug protection:	IP67

Cable length:	5 m

Cable connection:	one side with pre-configured plug
	one side with open cable ends

Version:	NFM0 ZVER PS

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pipe mounting system, suitable for temporary

installation of CSM flow velocity sensors and

DSM level sensors in pipelines from DN 150/160

to DN 300.

Material:	1.4571 (AISI 316Ti)

stainless spring steel

Nominal diameters:	DN 150/160 - DN 300

Version:	ZUB0 RMS3

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pipe mounting system, suitable for temporary

installation of CSM flow velocity sensors and

DSM level sensors in pipelines and egg-shaped

profiles up to DN 800.

Material:	1.4571 (AISI 316Ti)

stainless spring steel

Nominal diameters:	DN 160 - DN 800

Version:	ZUB0 RMS4

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pipe mounting system, suitable for temporary

installation of up to 3 CSM or CSP flow

velocity sensors and DSM level sensors in

pipelines from DN 800  to DN 2000

Material:	1.4571 (AISI 316Ti)

stainless spring steel

Nominal diameters:	DN 800 - DN 2000

Version:	ZUB0 RMS5

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

WEB Portal

Data remote transmission software

Device-related access for the web-based NIVUS

data collection system.

Data collection system with centralised data storage

and device communication.

Devices connecting with centre save readings and

status data in a centralised data bank.

Data security and availability according to current

IP security standards.

Transmitted readings are provided in the portal for

1 year and can be downloaded manually.

Device overview and device status are available in

the portal. Measurement spots can be localised on an

integrated map. Readings are saved in the data bank

using the recording frequency and can be recalled

by using an Internet browser.

The http server can be operated with any Internet browser

available on the market.

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: part of the transmitter standard delivery